## Slide 1
Patricia M. Dehmer Acting Director, Office of Science, U.S. Department of Energy
http://science.energy.gov/sc-2/presentations-and-testimony/
Energy Facts:
Energy challenges in a new era of science
University of Chicago
5 November 2013

## Slide 2: 400 Years of Energy Use in the U.S. 19th C discoveries and 20th C technologies are very much part of today’s infrastructure
Petroleum
1650
1700
1750
1800
1850
1900
1950
2000
10
20
30
40
0
Quadrillion Btu
U.S. Energy Consumption by Source
Wood
Hydroelectric
Power
Coal
Natural Gas
Nuclear Electric Power
10
20
30
40
0
Quadrillion Btu
Rural Electrification Act,
1935
Intercontinental Rail System, mid 1800s
Incandescent lamp,
1870s
Four-stroke combustion engine, 1870s
Watt Steam Engine, 1782
Eisenhower Highway System, 1956
Still >80% reliant on fossil fuels

## Slide 3
Today
Gas CH4
Oil CH2
Coal CH0.8
heat
combustion
useful work
Disposable fuels
Commodity materials
Sunlight
Wind
Water
Geothermal
Biomass
+
Storage
Transmission
CCS
Efficiency
Electricity
and
fuels
direct conversion
Future
Sustainable Energy = High Tech Materials Materials, Chemical Transformations, & Biology by (Computer-Aided) Design
3
useful work
High-tech materials, chemistry, biology, e.g., for photovoltaics, electrodes and electrolytes, smart membranes, separators, superconductors, catalysts, fuels, sensors, and novel piezoelectrics

## Slide 4: The “Basic Research Needs” Series 10 workshops; 5 years; more than 1,500 participants from academia, industry, and DOE labs
Control of materials properties and functionalities through atomic design: Science at the nanoscale
Designer catalysts, interfaces, membranes, bio-materials, …
Engineered microbes
Discovery, design, and synthesis of new materials, especially those that perform well under extreme conditions
New tools for atomic-level characterization and for computational modeling
Notes: CHARACTERISTICS OF A BASIC RESEARCH NEEDS WORKSHOP
Each workshop has three goals: (1) to summarize, prior to the workshop, the current state of technology and the associated R&D challenges in a Technology Perspectives Factual Document, which is used as a resource document for the basic research community at the workshop and well into the future; (2) to define a set of Proposed Research Directions that address the technology R&D challenges, the so-called technology show stoppers; and (3) to define a set of Science Grand Challenges that, if solved, might result in transformational changes in energy technologies.
The Basic Research Needs workshops must accomplish a great deal in a short time and their output must be authoritative, influential, and enduring. To accomplish the goals, the workshop planning, execution, and output stages are defined and structured. Ideally, each workshop report should serve as a reference document with a long shelf life. Additionally, the reports should be readily accessible. All reports are available on the BES website (http://www.sc.doe.gov/bes), usually within 60-75 days of the workshop.
The workshops are structured so that the participants learn about the status and challenges of a particular energy technology, generate proposed basic research directions to address short-term technology showstoppers, and articulate basic research grand challenges that might lead to transformational changes in energy technologies for the 21st century and beyond. The workshop reports that result from this process can help define the basic research agenda for a “decades-to-century” national energy agenda.
Workshop planning begins many months in advance and is performed by the workshop executive group, which is led by strong scientist chairs and co-chairs from academia and/or national laboratories. The executive group is made up of the workshop chair, co-chair(s), and panel leads. Participants come primarily from the scientific community and include the workshop chair(s), plenary speakers, panel leads, panelists, and writers. Each role is assigned tasks to complete before, during, and after the workshop. Technology experts serve as plenary speakers to provide applied perspectives to the scientific community.
A hallmark of the Basic Research Needs workshops is the production of the Technology Perspectives Factual Document. This feature describes the current status of technology development and is prepared prior to the workshop. It provides a common context and language for workshop discussions, it is used to educate workshop participants, and it becomes part of the workshop report. The Technology Perspectives Factual Document is written by technology experts from inside and outside DOE. If existing material is available (for example, technology roadmaps), it is included either explicitly or by reference. The Technology Perspectives Factual Document is not meant to provide the perspectives of the science community. Instead, science perspectives are garnered as an outcome of the workshop.
The outputs of the workshop are organized as (1) Panel Surveys describing the current state of science for each panel theme, (2) Priority Research Directions and Cross-Cutting Research Directions listed by each panel, (3) Science Grand Challenges outlined by all participants, and (4) Science and Technology Relationships Charts completed by the participants.
The result is a prioritization of the discovery-class and use-inspired basic research pertinent to energy technologies, obtained through a documented process. Often after the workshop, the chair and co-chair(s) and BES federal staff members participate in outreach activities to communicate the results of the workshop to the scientific community. Additionally, BES federal staff members brief other interested parties in the federal system, both inside and outside of DOE.

## Slide 5: Grand Challenge Questions in Materials and Chemistry
Synthesize, atom by atom, new forms of matter with tailored properties
Synthesize nanoscale objects with capabilities rivaling those of living things
Control the quantum behavior of electrons in materials
Control emergent properties that arise from the complex correlations of atomic and electronic constituents
Control matter far from equilibrium

## Slide 6
Banishing fear of
energy discussions

## Slide 7
“toe”
“quads”
BTU .. quad .. boe .. bboe .. toe .. tce .. Joule .. therm .. thermie .. calorie ..
Fear of Too Many Energy Units
7

## Slide 8: On-Line Energy Conversion Calculators Banish Fear of Units
8

## Slide 9: Prefixes and Names for Large and Small Numbers

## Slide 10
Metric Prefixes
10

## Slide 11
Energy sources and consumption sectors in the U.S.
Sankey Diagrams

## Slide 12
Domestic
Production:
78.1 Quads
Imports:
28.6 Quads
Consumption:
97.3 Quads
Exports:
10.4 Quads
Energy Supply (Quads)
Energy Consumption
U.S. Energy Flow, 2012
About 30% of U.S. primary energy is imported
Adjustments: -1
12
U.S. Share of World, 2007
Population
Energy
Production
Energy
Consumption
4.6%
15.0%
21.0%

## Slide 13
U.S. Energy Flow, 2011 (Quads)
>80% of primary energy is from fossil fuels
Supply
108
Quads
Domestic
73%
Imports
27%
Residential
Commercial
Industrial
Consume
98
Quads
Renewable 9%
Fossil
82%
Transportation
Nuclear 9%
13
Coal
Natural Gas
Crude Oil
Nuclear Electric Power
Renewable Energy
Petroleum
NGPL
Coal
Natural Gas
Petroleum
Nuclear Electric Power
Renewable Energy
Exports

## Slide 14
14
U.S. Energy Production and Use in 2012 Estimated Energy Use: ~95.1 Quads
Notes: “Zero Carbon Energy”

## Slide 15
U.S. Energy Flow, 1950 (Quads)
At midcentury, the U.S. used 1/3 of the primary energy used today and with greater overall efficiency
15
Today compared to 1950:
U.S. population ~2x that in 1950
Total primary energy ~3x that in 1950
Primary energy (petroleum) for transportation ~4x that in 1950
Primary energy for electricity generation ~10x that in 1950
Little or no imported petroleum in 1950
“Used” and “Wasted” energy were about equal in 1950 (Today: “Wasted” energy = 1.5x “Used” energy)

## Slide 16
Electricity Sources and End Uses
Conversion Losses
25 Quads
Gross Generation
15 Quads
Energy Consumed to
Generate Electricity
40 Quads
Residential
Commercial
Industrial
16

## Slide 17
Summary of Sources and Consumption Sectors (Quads)
17

## Slide 18
Overall Efficiency of an Incandescent Bulb  2%
Lighting accounts for 22% of all electricity usage in the U.S.
Example of energy lost during conversion and transmission. Imagine that the coal needed to illuminate an incandescent light bulb contains 100 units of energy when it enters the power plant. Only two units of energy eventually light the bulb. The remaining 98 units are lost along the way, primarily as heat.
2 units of energy in light output
Energy content of coal: 100 units
The Energy Independence and Security Act of 2007 requires light bulbs be 30% more energy efficient (similar to current halogen lamps) than current incandescent bulbs by 2012 to 2014. The efficiency standards start with 100-watt bulbs in January 2012 and end with 40-watt bulbs in January 2014. By 2020, all general-purpose bulbs must produce at least 45 lumens per watt (similar to current CFLs).
18
Question: Do you know how many light bulbs are in your house?

## Slide 19
World energy consumption

## Slide 20: World Energy Consumption 1990-2040 (Quads)
20
Energy Facts 2013
Some equivalent ways of referring to the energy used by the U.S. in 1 year (approx. 100 Quads)
100.0 quadrillion British Thermal Units (Quads) U.S. & British unit of energy
105.5 exa Joules (EJ) Metric unit of energy
3.346 terawatt-years (TW-yr) Metric unit of power (energy/sec)x(#seconds in a year)

## Slide 21
Growth in Global Energy Consumption Occurs Almost Exclusively in non-OECD Countries
World energy consumption, 1990-2040 (Quads)
Non-OECD energy consumption by country grouping, 1990-2040 (Quads)
21
Some equivalent ways of referring to the energy used by the U.S. in 1 year (approx. 100 Quads)
100.0 quadrillion British Thermal Units (Quads) U.S. & British unit of energy
105.5 exa Joules (EJ) Metric unit of energy
3.346 terawatt-years (TW-yr) Metric unit of power (energy/sec)x(#seconds in a year)

## Slide 22
World Regions and OECD Member Countries
The OECD is a forum of countries committed to democracy and the market economy, providing a setting to compare policy experiences, seek answers to common problems, identify good practices, and co-ordinate domestic and international policies. Twenty countries signed the Convention on the OECD on 14 December 1960; twelve additional countries have joined since.
22

## Slide 23
OECD Member Countries
AUSTRALIA: 7 June 1971 AUSTRIA: 29 September 1961 BELGIUM: 13 September 1961 CANADA: 10 April 1961 CHILE: 7 May 2010 CZECH REPUBLIC: 21 December 1995 DENMARK: 30 May 1961 FINLAND: 28 January 1969 FRANCE: 7 August 1961 GERMANY: 27 September 1961 GREECE: 27 September 1961 HUNGARY: 7 May 1996 ICELAND: 5 June 1961 IRELAND: 17 August 1961 ITALY: 29 March 1962 JAPAN: 28 April 1964 KOREA: 12 December 1996 LUXEMBOURG: 7 December 1961 MEXICO: 18 May 1994 NETHERLANDS: 13 November 1961 NEW ZEALAND: 29 May 1973 NORWAY: 4 July 1961 POLAND: 22 November 1996 PORTUGAL: 4 August 1961 SLOVAK REPUBLIC: 14 December 2000 SLOVENIA: 21 July 2010 SPAIN: 3 August 1961 SWEDEN: 28 September 1961 SWITZERLAND: 28 September 1961 TURKEY: 2 August 1961 UNITED KINGDOM: 2 May 1961 UNITED STATES: 12 April 1961
OECD MEMBER COUNTRIES
Twenty countries originally signed the Convention on the Organisation for Economic Co-operation and Development on 14 December 1960. Since then twelve countries have become members of the Organisation. The Member countries of the Organisation and the dates on which they deposited their instruments of ratification are:
23

## Slide 24
Energy needs in the 21st century
?
~100 Quads
U.S.
Chart: 
| Petroleum | Natural Gas | Coal | Nuclear | Renewables
 | 35.28 | 24.84 | 19.64 | 8.26 | 9.14
?
World
~500 Quads
Chart: 
| Petroleum | Natural Gas | Coal | Nuclear | Renewables
 | 163.9115 | 118.5377 | 148.0223 | 22.2385 | 42.4015

## Slide 25
U.S. Primary Energy Use by Fuel 1980-2040 Renewables and natural gas lead rise in primary energy consumption
25
Quads

## Slide 26
World energy consumption (Quads)
Projections to 2035 are from the Energy Information Administration, International Energy Outlook, 2010.
826
1,286
2050
2100
Projections for 2050 and 2100 are based on a scenario from the Intergovern-mental Panel on Climate Change (IPCC), an organization jointly established in 1988 by the World Meteorological Organization and the United Nations Environment Programme. The IPCC provides comprehensive assessments of information relevant to human-induced climate change. The scenario chosen is based on “moderate” assumptions (Scenario B2) for population and economic growth and hence is neither overly conservative nor overly aggressive.
World Energy Needs will Grow in the 21st Century
26

## Slide 27
Petroleum 37%
Coal 21%
Natural Gas 25%
Nuclear 9%
Renewables 8%
Fossil fuels

## Slide 28
Fossil Fuel Supplies are Estimated using Reserves-to-Production (R/P) Ratios
Proven World Reserves-to-Production Ratio at End 2012 (Years)
The R/P ratio is the number of years that proved reserves would last at current production rates.
100
200
300
400
500
28
OECD
Non-OECD
European Union
Former Soviet Union
World
Notes: “BP Statistical Review of World Energy 2005,” http://www.bp.com/liveassets/bp_internet/globalbp/globalbp_uk_english/publications/energy_reviews_2005/STAGING/local_assets/downloads/pdf/statistical_review_of_world_energy_full_report_2005.pdf
Slide Courtesy: Steven E. Koonin, Chief Scientist, BP, plc

## Slide 29
World Reserves of Oil There is a significant dislocation between fossil fuel supply and demand
(http://www.energybulletin.net/37329.html)
Who uses the oil?
(thousands of barrels per day)
29
Notes: “BP Statistical Review of World Energy 2005,” http://www.bp.com/liveassets/bp_internet/globalbp/globalbp_uk_english/publications/energy_reviews_2005/STAGING/local_assets/downloads/pdf/statistical_review_of_world_energy_full_report_2005.pdf
Slide Courtesy: Steven E. Koonin, Chief Scientist, BP, plc

## Slide 30
U.S. Natural Gas Production Showing Increase in Shale Gas
Trillion cubic feet per year
30

## Slide 31
Unconventional Gas: Shale Gas

## Slide 32
Tight Gas vs. Shale Gas
32

## Slide 33
Nuclear energy
Petroleum 37%
Coal 21%
Natural Gas 25%
Nuclear 9%
Renewables 8%

## Slide 34
Units Ordered
Construction Permits Issued
Full-power Operating Licenses
Operable Units
Shutdowns
1955
1960
1965
1970
1975
1980
1985
1990
1995
2000
0
50
100
150
200
250
300
Number of Units
Year
Permits for U.S. Reactors Issued Only Until 1979 8.4 quads of nuclear energy produced by 104 operable nuclear power plants
34

## Slide 35
35
Nuclear Energy Provides 20% of U.S. Electricity
Europe and Japan rely much more heavily on nuclear energy for electricity generation

## Slide 36
Renewables
Petroleum 36%
Coal
20%
Natural Gas 26%
Nuclear 8%
Renewables 9%

## Slide 37
Nuclear and Renewable are ~17% of Energy Supply Hydroelectric and wood still dominate the renewable energies
Petroleum 36%
Coal
20%
Natural Gas 26%
Nuclear 8%
Renewables 9%
37

## Slide 38
Renewable Energy Consumption and Major Sources
38

## Slide 39
Generation and Use of Wind and Solar Energy
Separation between renewable sources and demand centers requires new long distance transmission lines.
39
Demand
Demand
Wind
Wind
Sun
http://visibleearth.nasa.gov/view_rec.php?id=1438l
Chart adapted from the American Physical Society report, Integrating Renewable Energy on the Grid

## Slide 40
Energy and the environment

## Slide 41
How do the Earth's land, water, air, and life interact to affect the environment?
41

## Slide 42
Modern CO2 Concentrations are Increasing
The current concentration is the highest in 800,000 years, as determined by ice core data
Concentration prior to 1800 was ~280 ppm
Concentration now ~395 ppm. Under a “business-as-usual” scenario, concentration could rise to 1,000 ppm
42
Monthly mean atmospheric carbon dioxide at Mauna Loa Observatory, Hawaii. The carbon dioxide data (red curve) are the longest record of direct measurements of CO2 in the atmosphere. Begun by C. David Keeling of the Scripps Institution of Oceanography in March of 1958, they have been continued by NOAA since May of 1974. The black curve is the seasonally corrected data.

## Slide 43
Nature, 15 May 2008 The air bubbles trapped in the Antarctic Vostok and EPICA Dome C ice cores provide composite records of levels of atmospheric carbon dioxide and methane for the past 800,000 years.
The fundamental conclusion is that today's concentrations of these greenhouse gases have no past analogue in the ice-core record. Concentrations do not rise above pre-industrial revolution values.
The general long-term behavior of methane and carbon dioxide, following patterns driven by slow changes in Earth's orbit, continues throughout the older sections of the records.
Bubbles – 800,000 Years of CO2 Concentrations
43

## Slide 44
CO2 Concentrations and Temperature
The correlation extends throughout the 800,000-year time span of the ice core data
a The 800,000-year records of atmospheric carbon dioxide (red; parts per million, p.p.m.) and methane (green; parts per billion, p.p.b.) from the EPICA Dome C ice core together with a temperature reconstruction (relative to the average of the past millennium) based on the deuterium–hydrogen ratio of the ice, reinforce the tight coupling between greenhouse-gas concentrations and climate observed in previous, shorter records. Concentrations of greenhouse gases in the modern atmosphere are highly anomalous with respect to natural greenhouse-gas variations (present-day concentrations are around 380 p.p.m. for carbon dioxide and 1,800 p.p.b. for methane).
b The carbon dioxide and methane trends from the past 2,000 years.
E.J. Brook, Nature 453, 291 (2008).
44

## Slide 45
Past and Future CO2 Concentrations
IPCC Fifth Assessment Report, WG 1, Climate Change 2013: The Physical Science Basis
45

## Slide 46
Past and Future CO2 Concentrations
CO2 concentrations are predicted to increase by a factor of two to three
46
395

## Slide 47
Natural Variations in the Earth’s Orbit Affect Climate
and Greenhouse Gas Concentrations
There are three orbital perturbations with five periods: eccentricity (at 400 and 100 ky); obliquity (41 ky); and precession (23 and 19 ky). (A) Eccentricity refers to the shape of Earth’s orbit around the sun, varying from near circular to elliptical. (B) Obliquity refers to the tilt of Earth’s axis relative to the plane of the ecliptic, varying between 22.1o and 24.5o. A high angle of tilt increases the seasonal contrast, most effectively at high latitudes. (C) Precession refers to the wobble of the axis of rotation describing a circle in space with a period of 26 ky. Modulated by orbital eccentricity, precession determines where on the orbit around the sun seasons occur, thereby increasing the seasonal contrast in one hemisphere and decreasing it in the other. The periods of the precessional signal modulated by eccentricity are 23 and 19 ky.
James Zachos, Mark Pagani, Lisa Sloan, Ellen Thomas, and Katharina Billups, Science 292, 4 (2001).
W. F. Ruddiman, Scientific American, March 2005, p. 46

## Slide 48: Planets, Atmospheres, and Climate
= -58oF
= 59oF
= 788 oF
Sun
A planet's climate is determined by its mass, its distance from the sun, and the composition of its atmosphere. Earth's atmosphere is 78% nitrogen, 21% oxygen, and 1% other gases. Carbon dioxide accounts for 0.03 - 0.04%. Water vapor, carbon dioxide, and other minor gases absorb thermal radiation leaving the surface. These greenhouse gases act as a partial blanket for the thermal radiation from the surface and enable it to be substantially warmer than it would otherwise be. Without the greenhouse gases, Earth's average temperature would be roughly -20°C = -4 °F.
48
Notes: A planet's climate is decided by its mass, its distance from the sun and the composition of its atmosphere. Mars is too small to keep a thick atmosphere. Its atmosphere consists mainly of carbon dioxide, but the atmosphere is very thin. The atmosphere of the Earth is a hundred times thicker. Most of Mars' carbon dioxide is frozen in the ground. Mars' average surface temperature is about -50°C. Venus has almost the same mass as Earth but a thicker atmosphere, composed of 96% carbon dioxide. The surface temperature on Venus is +460°C. Earth's atmosphere is 78% nitrogen, 21% oxygen, and 1% other gases. Carbon dioxide accounts for just 0.03 - 0.04%. Water vapour, varying in amount from 0 to 2%, carbon dioxide and some other minor gases present in the atmosphere absorb some of the thermal radiation leaving the surface and emit radiation from much higher and colder levels out to space. These radiatively active gases are known as greenhouse gases because they act as a partial blanket for the thermal radiation from the surface and enable it to be substantially warmer than it would otherwise be, analogous to the effect of a greenhouse. This blanketing is known as the natural greenhous effect. Without the greenhouse gases, Earth's average temperature would be roughly -20°C. The climates on Mars and Venus are very different, but very stable and highly predictable. The Earth's climate is unstable and rather unpredictable as compared with that of the other two planets.
Planets and atmospheres. (2000). In UNEP/GRID-Arendal Maps and Graphics Library. Retrieved from http://maps.grida.no/go/graphic/planets_and_atmospheres.

## Slide 49
Solar Energy Cycle
And the Greenhouse Effect
Notes: THE FLOW OF ENERGY THROUGH THE CLIMATE SYSTEM
A suite of papers has provided updated estimates of trends, variability, mean and annual cycle of energy flowing through the climate system, and energy storage, release, and transport in the atmosphere, ocean, and land surface. The estimates are obtained from recent observations using the latest datasets ([1]-[5]). The results indicate that the global energy budget can now be estimated reasonably well, with the largest continuing sources of uncertainty being the ocean heat budget south of about 35S. The current imbalance in radiation at the top-of-atmosphere owing to human-induced increases in greenhouse gases means that the atmosphere, land and ocean are warming up, and ice is melting, leading to a rise in sea level. A holistic integrated approach that brings all information to bear provides constraints on what is happening and where the main weaknesses are in the current observing system. These analyses also provide insights into both top-of-atmosphere and surface balances and model problems. For instance, the results indicate that climate models typically have too much downward longwave radiation, which is compensated by too much evaporation and precipitation.
Figure: From Trenberth et al (2008) shows the estimated global mean energy flows for the 2000 to 2004 time frame.
Fasullo, J. T., and K. E. Trenberth, 2008: The annual cycle of the energy budget. Part I: Global mean and land-ocean exchanges. J. Climate, 21, 2297-2312.
Fasullo, J. T., and K. E. Trenberth, 2008: The annual cycle of the energy budget. Part II: Meridional structures and poleward transports. J. Climate, 21, 2313-2325.
Trenberth, K. E., and L. Smith, 2008: The three dimensional structure of the atmospheric energy budget: methodology and evaluation. Climate Dynamics, in press. doi:10.1007/s00382-008-0389-3.
Trenberth, K. E., and L. Smith, 2008: Atmospheric energy budgets in the Japanese Reanalysis: Evaluation and variability. J. Meteor. Soc. Japan, in press.
Trenberth, K. E., J. T. Fasullo, and J. Kiehl, 2008: Earth's global energy budget. Bull. Amer. Meteor. Soc., in press.
Several recent presentations by Trenberth may be found at http://www.cgd.ucar.edu/cas/Trenberth/trenberth_presentations.html

## Slide 50
Radiation Transmitted by the Atmosphere
Atmospheric Window
50

## Slide 51
51
Carbon Cycle
Atmosphere = 800 GtC

## Slide 52
52

## Slide 53
53
Simplified Schematic of the Global Carbon Cycle IPCC Fifth Assessment Report, WG 1, Climate Change 2013: The Physical Science Basis

## Slide 54
Proxies for Climate Change

## Slide 55: Proxies for Climate Change
Preserved physical characteristics of the past that enable reconstruction of past climatic conditions. The deposition or growth rates of the proxies' material is influenced by the climatic conditions of the time in which they were laid down or grew. Examples of proxies include ice cores, tree rings, boreholes, corals, land & sea ice, and lake and ocean sediments.
55

## Slide 56
56
56
Notes: Time Magazine, Special Report on Global Warming, April 3, 2006.

## Slide 57: Greenland Ice Mass Loss – 2002 to 2009
I. Velicogna, GEOPHYSICAL RESEARCH LETTERS, VOL. 36, L19503, doi:10.1029/2009GL040222, 2009
Increasing rates of ice mass loss from the Greenland and Antarctic ice sheets revealed by GRACE (Gravity Recovery and Climate Experiment) satellite
In Greenland, the mass loss increased from 137 Gt/yr in 2002–2003 to 286 Gt/yr in 2007–2009
In Antarctica, the mass loss increased from 104 Gt/yr in 2002–2006 to 246 Gt/yr in 2006–2009
Time series of ice mass changes for the Greenland ice sheet estimated from GRACE monthly mass solutions for the period from April 2002 to February 2009. Unfiltered data are blue crosses. Data filtered for the seasonal dependence using a 13-month window are shown as red crosses. The best-fitting quadratic trend is shown (green line). The GRACE data have been corrected for leakage and GIA.
57

## Slide 58: Gravity Recovery and Climate Experiment (GRACE)
GRACE uses a microwave ranging system to measure changes in the speed and distance between two identical spacecraft flying about 220 kilometers apart, 500 kilometers above Earth. Separation changes as small as 10 microns—about one-tenth the width of a human hair—can be detected.
GRACE satellites can sense minute variations in Earth's gravitational pull. When the first satellite passes over a region of slightly stronger gravity, it is pulled ahead of the trailing satellite, causing the distance between the satellites to increase.
By measuring the changing distance between the two satellites and combining that data with positioning measurements from GPS instruments, a gravity map can be constructed.
58

## Slide 59: How GRACE Works
GRACE uses a microwave ranging system to measure changes in the speed and distance between two identical spacecraft flying in a polar orbit about 220 kilometers apart, 500 kilometers above Earth. The ranging system can detect separation changes as small as 10 microns over a distance of 220 kilometers.
As the GRACE satellites circle the globe 16 times a day, they sense minute variations in Earth's gravitational pull. When the first satellite passes over a region of slightly stronger gravity, a gravity anomaly, it is pulled slightly ahead of the trailing satellite. This causes the distance between the satellites to increase. The first spacecraft then passes the anomaly, and slows down again; meanwhile the following spacecraft accelerates, then decelerates over the same point.
By measuring the constantly changing distance between the two satellites and combining that data with precise positioning measurements from Global Positioning System (GPS) instruments, scientists can construct a detailed map of Earth's gravity.
The two satellites (nicknamed "Tom" and "Jerry") constantly maintain a two-way microwave-ranging link between them. Fine distance measurements are made by comparing frequency shifts of the link. As a cross-check, the vehicles measure their own movements using accelerometers. All of this information is then downloaded to ground stations. To establish baseline positions and fulfill housekeeping functions, the satellites also use star cameras, magnetometers, and GPS receivers. The GRACE vehicles also have optical corner reflectors to enable laser ranging from ground stations, bridging the range between spacecraft positions and Doppler ranges.
59
Notes: Sec. Chu has pic of two satellites; missing estimate of sea level rise; consider 14C/12C story

## Slide 60
Climate Modeling

## Slide 61: Types of Climate Models
Global Climate Models: Based on general circulation models (GCMS) driven by physical forcing in the atmosphere and oceans Earth System Models: Couple individual process models (e.g., atmosphere, land, ocean, sea ice, carbon, and sulfur cycles) | Integrated Assessment Models: Understand and model the complex interactions of human and natural systems Regional Models: Models at scales that are useful for regional and local planners
10km
IPCC AR5
2010
61

## Slide 62: Global Climate Models
First type of climate model, pioneered by DOE supported scientists in the 1980s
Based on general circulation models (GCMs) that describe physics of atmospheric and ocean circulation
More recently, land surface and sea ice have been included in GCMs
Spatial resolution is currently 10–100 km
62

## Slide 63: Earth System Models
Highly coupled models that incorporate information from GCMs as well as
  Biogeochemical cycles (carbon and sulfur)
  Atmospheric chemistry (a variety of active species)
  Land models include dynamic vegetation
  Spatial resolution is currently similar to GCMs
63

## Slide 64: Integrated Assessment Models
Assessing human interactions with nature and the role of human decision-making
Scenarios involve changes in energy sources, energy policy, and economics
Current conditions
  Continental or country scales
  Strongly assumption driven
Beginning to address emerging interest in impacts, adaptation, and vulnerabilities
64

## Slide 65: Regional Climate Models
Typically at scale 1–50 km
May be derived in 2 different ways:
  “Bottom up” approach incorporating regional and local scale data—adapted from regional forecast models
  “Top down” approach, downscaling from Global or Earth System model
In demand by regional and local planners
65

## Slide 66: Evolution of Climate Models
Global Climate Models
Earth System Models
DOE contributions
✔
✔
✔
✔
✔
✔
✔
✔
66

## Slide 67
CO2 Concentration, Temperature, and Sea Level Rise Long after Emissions are Reduced
Now
100 yrs
1,000 yrs
Sea-level rise due to ice melting
Sea-level rise due to thermal expansion
Temp stabilization
CO2 stabilization
CO2 emissions
Assume anthropogenic CO2 emissions peak in 0-100 years, then drop off to near zero
67

## Slide 68: Recent Predictions of Climate Models
68

## Slide 69
IPCC Socioeconomic Scenarios for Climate Modeling
69

## Slide 70: Scenarios from the U.S. Climate Change Science Program Report “Scenarios of Greenhouse Gas Emissions and Atmospheric Concentrations”
Integrated Assessment Models – include both physical and social science models that consider demographic, political, and economic variables that affect greenhouse gas emission scenarios in addition to the physical climate system (atmosphere, oceans, and terrestrial biosphere).
The Integrated Global Systems Model (IGSM) [MIT]
Model for Evaluating the Regional and Global Effects (MERGE) of GHG Reduction Policies [Stanford University and EPRI]
The MiniCAM Model of the Joint Global Change Research Institute [PNNL and the University of Maryland]
70

## Slide 71
IGSM
MERGE
MiniCAM
450 ppmv CO2
Reference Scenarios
U.S Primary Energy Consumption by Fuels Across Scenarios
71

## Slide 72
Components of Research

## Slide 73: A Research Strategy
73
Nanostructured thin-film organic photovoltaic devices
Artificial
Photosynthesis
Capture or separation of CO2 from gas mixtures
Structure of lignocellulose at the nanoscale and the rules by which plants create this material
Lightweight structural materials for transportation
Radiation-resistant Materials
High-Tc and high current superconductors for grid and other electrical applications
Conversion of electricity to light using new designs, such as luminescent nanowires, quantum dots, and hybrid architectures;
Sequestration of CO2 underland
Notes: “Zero Carbon Energy”

## Slide 74
How to Buy a Light Bulb

## Slide 75
Lighting Tutorial

## Slide 76
Shape of glass bulb/size of base
Type: Incandescent, halogen, fluorescent, LED
Brightness (lumens)
Color (K)
Color rendition index
Energy (watts)
Efficacy (lumens/watt) … and …
Efficiency (%)
Cost
Life expectancy (hours or years, sometimes assuming 1,000 hours/year)
Life cycle cost: Initial purchase price and price of energy to operate
Health/Safety
Instant on/Buzz/Dimmable/3-Way
Decisions when purchasing a light bulb

## Slide 78
Brightness (lumens)
The lumen (symbol: lm) is the SI derived unit of luminous flux, a measure of the total "amount" of visible light emitted by a source. Luminous flux depends on nominal response of the human eye to different wavelengths as represented by the luminosity function.
The lumen is defined in relation to the candela as
  1 lm = 1 cd · sr
The candela is the luminous intensity, in a given direction, of a source that emits monochromatic radiation of frequency 540 x 1012 hertz (555 nm) and that has a radiant intensity in that direction of 1/683 watt per steradian.

## Slide 82
All CFLs are 100 watt replacements, ranging from 23 to 26 watt
100 watt soft white incandescent
2700K CFL
3500K CFL
4100K CFL
5500K CFL
6500K CFL

## Slide 83
Color Rendering Index (CRI)
The CRI measures the ability of a light source to reproduce the colors of objects faithfully in comparison with an ideal (blackbody) light source or natural light source.
Blackbody radiation has a CRI of 100; incandescent lamps have that rating, because they are almost blackbody radiators.
An ideal light source for color rendering will have both a color temperature similar to daylight and a high CRI value.
Notes: Lighting technologies are substitutes for sunlight in the 425-675 nm spectral region where sunlight is most concentrated and to which the human eye has evolved to be most sensitive. The history of lighting can be viewed as the development of increasingly efficient technologies for creating visible light inside, but not wasted light outside, of that spectral region.
A 200-year perspective on that history is shown in the figure. The left axis indicates luminous efficacy, in units of lumens (a measure of light which factors in the human visual response to various wavelengths) per watt. The right axis indicates the corresponding power-conversion efficiency for a tri-LED tri-color white light source with moderate color rendering (CRI=80) and relatively warm color temperature (CCT=3900K). For such a source, 400lm/W would correspond to 100% power-conversion efficiency.
The three traditional technologies are fire; incandescence; and fluorescence and high-intensity discharges (HID). These three traditional technologies have all made significant progress over the past 200 years, but appear to be saturating at efficiencies in the 1-25% range.
A new, fourth technology is solid-state lighting. In principle, the technology is simple: electrons and holes are injected into a forward-biased semiconductor p-n junction; they recombine creating photons; the resulting photons are extracted from the chip; then the photons are either mixed with different-color photons from other LEDs, or are energy down-converted into a distribution of colors using phosphors or other down-conversion materials, with the colors chosen so as to create the appearance of white.
In practice, there are losses at every step of the way, and efficiently creating white light from semiconductor materials with band-gaps that span the visible spectrum is extremely challenging. Nevertheless, great strides are being made, and SSL-LED technology is currently on a very rapid improvement curve, particularly the red, green and blue monochrome lamps necessary for white light.

## Slide 84
Color Rendering Index (CRI) made easier
Two different light spectra that have the same effect on the three color receptors in the human eye will be perceived as the same color.
Daylight, which has a continuous spectrum
White light emitted by fluorescent lamps, which has a spectrum of a few bands
The human eye cannot tell the difference between such light spectra by looking into the light source, but reflected colors from objects can look different.
Notes: Lighting technologies are substitutes for sunlight in the 425-675 nm spectral region where sunlight is most concentrated and to which the human eye has evolved to be most sensitive. The history of lighting can be viewed as the development of increasingly efficient technologies for creating visible light inside, but not wasted light outside, of that spectral region.
A 200-year perspective on that history is shown in the figure. The left axis indicates luminous efficacy, in units of lumens (a measure of light which factors in the human visual response to various wavelengths) per watt. The right axis indicates the corresponding power-conversion efficiency for a tri-LED tri-color white light source with moderate color rendering (CRI=80) and relatively warm color temperature (CCT=3900K). For such a source, 400lm/W would correspond to 100% power-conversion efficiency.
The three traditional technologies are fire; incandescence; and fluorescence and high-intensity discharges (HID). These three traditional technologies have all made significant progress over the past 200 years, but appear to be saturating at efficiencies in the 1-25% range.
A new, fourth technology is solid-state lighting. In principle, the technology is simple: electrons and holes are injected into a forward-biased semiconductor p-n junction; they recombine creating photons; the resulting photons are extracted from the chip; then the photons are either mixed with different-color photons from other LEDs, or are energy down-converted into a distribution of colors using phosphors or other down-conversion materials, with the colors chosen so as to create the appearance of white.
In practice, there are losses at every step of the way, and efficiently creating white light from semiconductor materials with band-gaps that span the visible spectrum is extremely challenging. Nevertheless, great strides are being made, and SSL-LED technology is currently on a very rapid improvement curve, particularly the red, green and blue monochrome lamps necessary for white light.

## Slide 85
Color Rendering Index
Notes: Lighting technologies are substitutes for sunlight in the 425-675 nm spectral region where sunlight is most concentrated and to which the human eye has evolved to be most sensitive. The history of lighting can be viewed as the development of increasingly efficient technologies for creating visible light inside, but not wasted light outside, of that spectral region.
A 200-year perspective on that history is shown in the figure. The left axis indicates luminous efficacy, in units of lumens (a measure of light which factors in the human visual response to various wavelengths) per watt. The right axis indicates the corresponding power-conversion efficiency for a tri-LED tri-color white light source with moderate color rendering (CRI=80) and relatively warm color temperature (CCT=3900K). For such a source, 400lm/W would correspond to 100% power-conversion efficiency.
The three traditional technologies are fire; incandescence; and fluorescence and high-intensity discharges (HID). These three traditional technologies have all made significant progress over the past 200 years, but appear to be saturating at efficiencies in the 1-25% range.
A new, fourth technology is solid-state lighting. In principle, the technology is simple: electrons and holes are injected into a forward-biased semiconductor p-n junction; they recombine creating photons; the resulting photons are extracted from the chip; then the photons are either mixed with different-color photons from other LEDs, or are energy down-converted into a distribution of colors using phosphors or other down-conversion materials, with the colors chosen so as to create the appearance of white.
In practice, there are losses at every step of the way, and efficiently creating white light from semiconductor materials with band-gaps that span the visible spectrum is extremely challenging. Nevertheless, great strides are being made, and SSL-LED technology is currently on a very rapid improvement curve, particularly the red, green and blue monochrome lamps necessary for white light.

## Slide 86
Luminous efficacy vs. efficiency for a light source
Luminous efficacy is the ratio of the luminous flux emitted (lumens) to the input power (watts).
But, remember, luminous flux depends on response of the human eye to different wavelengths as represented by the luminosity function.
When expressed as a fraction of the maximum possible luminous efficacy (i.e., uncorrected for the response of the eye), this is called lighting efficiency.

## Slide 87
Luminous efficacy (lumens/watt) for various light sources

## Slide 88
3
Jeff Y. Tsao, “Solid-State Lighting: Lamps, Chips and Materials for Tomorrow,” IEEE Circuits & Devices 20(3), 28-37 (2004).
Luminous efficacy (lumens/watt) for various light sources
88
Notes: Lighting technologies are substitutes for sunlight in the 425-675 nm spectral region where sunlight is most concentrated and to which the human eye has evolved to be most sensitive. The history of lighting can be viewed as the development of increasingly efficient technologies for creating visible light inside, but not wasted light outside, of that spectral region.
A 200-year perspective on that history is shown in the figure. The left axis indicates luminous efficacy, in units of lumens (a measure of light which factors in the human visual response to various wavelengths) per watt. The right axis indicates the corresponding power-conversion efficiency for a tri-LED tri-color white light source with moderate color rendering (CRI=80) and relatively warm color temperature (CCT=3900K). For such a source, 400lm/W would correspond to 100% power-conversion efficiency.
The three traditional technologies are fire; incandescence; and fluorescence and high-intensity discharges (HID). These three traditional technologies have all made significant progress over the past 200 years, but appear to be saturating at efficiencies in the 1-25% range.
A new, fourth technology is solid-state lighting. In principle, the technology is simple: electrons and holes are injected into a forward-biased semiconductor p-n junction; they recombine creating photons; the resulting photons are extracted from the chip; then the photons are either mixed with different-color photons from other LEDs, or are energy down-converted into a distribution of colors using phosphors or other down-conversion materials, with the colors chosen so as to create the appearance of white.
In practice, there are losses at every step of the way, and efficiently creating white light from semiconductor materials with band-gaps that span the visible spectrum is extremely challenging. Nevertheless, great strides are being made, and SSL-LED technology is currently on a very rapid improvement curve, particularly the red, green and blue monochrome lamps necessary for white light.

## Slide 89
Luminous efficacy vs. efficiency for light sources

## Slide 90
Traditional
incandescent
Halogen
incandescent
Compact
fluorescent (CFL)
Light-emitting
diode (LED)
Approximate wattage to produce 1,600 lumens
100
watts
77
watts
23
watts
20
watts
1,600
lumens
1,600
lumens
1,600
lumens
1,600
lumens

## Slide 91
For LEDs: Packaging Labels Provide the Facts
91
Notes: “Zero Carbon Energy”

## Slide 92
For CFLs: Packaging Labels Provide Similar Facts

## Slide 93
The End